deltarobot Message Format
Specification v1.0

Lucas Pires Camargo
EMB5613 – Projeto Integrado de Sistemas Embarcados
Prof. Diego Santos Greff

# Introduction
This document defines the message formats used by deltarobot. They are to be used in the implementation of both the firmware and the accompanying software interface.
For more information on the nature of the project and the robot itself, please refer to the full report.
## Purpose
The project aims for making the platform fully operational, which means giving the user means of controlling the platform position. This could be accomplished with an interface on the controller device itself, but we figure it is better (and more simply) done by use of a personal computer connected to the platform. This makes possible the use of an user interface with interactive 3D graphics, the creation of a software library for integration into other applications, path drawing, etc.
However, to accomplish this, there must be a standardized way for the controller to talk to a personal computer. Therefore, it was decided that a simple protocol would have to be defined.
## Definitions
In this specification, “Controller” means the device that operates the motors of the parallel actuators, reads sensor inputs, and executes the control loop. “Interface”, “Interface software”, or “Computer” refers to the computer that is communicating with the Controller, monitoring its status, and defining its goal positions.
An “Opcode” is be understood as “Operation code”. Different Opcodes describe the various functionalites of the protocol in compartmentalized commands.
## About this specification
This document is organized as follows:
- Section “Connection and Transmission” gives an overview on the physical link layer.
- Section “Message Frame Structure” defines the basic structure of a command.
- Section “Opcodes” defines commands, their requirements and outcomes.
- Section “Implementation Notes” gives further details in regards to implementation and noteworthy behaviors.

# Connection and Transmission
The Controller is to be connected to the Computer by means of a serial port device. This device has to be configured as follows:
- Baud rate: 115200 baud
- Data bits: 8 bits
- Stop bits: 1 bit
- Parity bits: (none)
- Hardware flow control: (disabled)
Furthermore, a “serial port”, this can mean a physical, standard RS-232 connection, or a connection emulated in software or in hardware. A valid implementation is a USB connection through which a serial data stream is sent, and that the Computer can recognize as such. This has to translate into a COM port or TTY device file (“/dev/ttyS?”, “/dev/ttyUSB?”) in the operating system of the Computer, to which the Interface Software connects.
TODO: Waveforms for byte transmission
# Message Frame Structure
Commands, status information, and control information are organized into frames. A frame is a validated sequence of bytes structured as follows:
Start-of-Frame	Length	Opcode	Data	Checksum	Terminator
‘$’ (ASCII)	Size in bytes (whole frame)	“What the frame is”	Opcode-dependant	(Mod-sum of frame bytes)	‘:’ (ASCII)
1 byte	1 byte	1 byte	(length – 5) bytes	1 byte	1 byte

TODO: descrição de cada campo passo-a-passo do negócio
## Checksum Calculation
TODO: descrever como é calculado o checksum
TODO: adicionar exemplo
## Notes
There is no message resend requests.
Incomplete or corrupted packets are lost.
If an ACK is times out an operation can be repeated depending on the opcode

# Opcodes
This section describes each opcode in detail. However, for the purpose of an overview, a complete list is given beforehand. The opcodes are divided in three categories: “common” opcodes that can be sent in both directions, “down” opcodes that only make sense from Computer to Controller, and “up” opcodes that only apply in the Controller to Computer direction.
Following the lists of opcodes, there is a section explaining each opcode in detail.
## List of Common Opcodes
- Acknowledge – 0x41 – ASCII ‘A’
- No-Acknowledge – 0x4E – ASCII ‘N’
## List of Down Opcodes
- Homing Request – 0x48 – ASCII ‘H’
- Status Request – 0x53 – ASCII ‘S’
- Move Request – 0x4D – ASCII ‘M’
- Cancel Request – 0x43 – ASCII ‘C’
## List of Up Opcodes
- Homing Finished – 0x68 – ASCII ‘h’
- Status Report – 0x73 – ASCII ‘s’
- Move Finished – 0x6D – ASCII ‘m’
- General Error – 0x65 – ASCII ‘e’
## Acknowledge – 0x41 – ‘A’
Description: This opcode is a general acknowledgement (ack) message, to be issued in response to a previous request. It depends on the specific request (opcode) if it requires a corresponding ack or not. The message signifies that the request was understood, considered valid, and will be attempted to be fulfilled. If that is not the case, a No-Acknowledge (0x4E) is to be issued instead.
Data length: 1 byte
Data fields:
Data
Original Opcode
1 byte

There is only a single data field: one byte containing the opcode that prompted the Acknowledge.
Expected behavior: Opcode-specific. Generally none.
## No-Acknowledge – 0x4E – ‘N’
Description: This opcode is a general non-acknowledgement (nack) message, to be issued in response to a previous request. It depends on the specific request (opcode) if it requires a corresponding ack/nack or not. The message signifies that the request was not understood, considered invalid, or can’t be fulfilled at this current time. It is the negative alternative to the Acknowledge (0x41) opcode.
Data length: 1 byte
Data fields:
Data
Original Opcode
1 byte

There is only a single data field: one byte containing the opcode that prompted the No-Acknowledge.
Expected behavior: Opcode-specific. Generally none.
## Homing Request – 0x48 – ‘H’
Description: This opcode is a request for the Controller to home in the actuators to a known default state. The specific behavior depends on the controller implementation, but is is expected to be something similar to retracting the arms until the stops are reached, defining the zero-movement state.
Data length: 0 bytes (none)
Data fields: This opcode has no associated data fields.
## Move Request – 0x4D – ‘M’
Description: This opcode is a request for the Controller to move the platform to a specified position. The path followed is expected to be linear.
Data length: TBD
Data fields:
This opcode has the following data fields:
Data
DA – float	DB – float	DC – float
4 bytes	4 bytes	4 bytes

- Data field DA – displacement of arm “A” – 4 bytes – IEEE 32-bit float
- Data field DB – displacement of arm “B” – 4 bytes – IEEE 32-bit float
- Data field DC – displacement of arm “C” – 4 bytes – IEEE 32-bit float